Watershed Outlet Monitoring Program

Willow Creek Station

# Burnsville, MN

Quarterly Report

## Preliminary Data

## July – September 2007

Prepared By: Dakota County Soil and Water Conservation District

### Prepared For: Lower Minnesota River Watershed District

##### October 2007

#### Introduction

The Willow Creek WOMP site, located in Burnsville behind the Menards on Hwy. 13, has been in operation since 1999.  The Willow Creek watershed drains more than 5,000 acres of various types of land uses including residential, vacant/agricultural, and commercial properties (Appendix A).  This report summarizes the results of flow, precipitation, and water quality for the 3rd quarter of 2007.  This data is preliminary and is subject to change until the Metropolitan Council submits the final report for this period.

#### Flow and Precipitation

Average flow in Willow Creek was 5.84 cubic feet per second (cfs) or 3.77 million gallons per day (mgd) (Table 1).  A graph describing quarterly flow and precipitation results is also provided (Figure 1).  It should be noted that the stage monitoring equipment was replaced in mid-September, which corresponds with a temporary decrease in stage observed in Figure 1.

Table 1. Average flow and total precipitation at Willow Creek WOMP Station July – September 2007

| Period | Average Flow (cfs/mgd) | Precipitation (inches) | *Average Monthly Precipitation, 1997-2006 (inches) |
| --- | --- | --- | --- |
| JULY | 0.55/0.36 | 1.05 | 4.28 |
| AUGUST | 11.97/7.74 | 8.41 | 4.29 |
| SEPTEMBER | 4.82/3.12 | 3.12 | 3.00 |
| TOTAL QUARTER | 5.84/3.77 | 12.58 | 11.57 |

*Average monthly precipitation data obtained from the National Weather Service station located near the Willow WOMP site.

#### Figure 1. Flow and precipitation at Willow WOMP Station July-September 2007

#### Water Quality

Five event composite samples (7/3/07, 7/8/07, 8/11/07, 8/13/07, 8/18/07), one event grab sample (9/19/07-due to equipment failure), and three low flow grab samples were collected at the Willow WOMP Station during the 3rd quarter of 2007.  Overall, water quality was good with most parameters below the state standard (in compliance with standards) or near the ecoregion mean (Table 2).  However, several endpoints showed unusually elevated results (highlighted red).  These results are likely due to the large number of August rain events and a reflection of the pollutant load present in the initial flush of storm water runoff.

Table 2. Average concentrations at Willow Creek WOMP Station January – June 2007 (for comparison purposes) and July-September 2007.

| Parameter | 1st quarter 2007 Ave. Concentration | 2nd Quarter 2007 Ave. Concentration | 3rd Quarter 2007 Ave. Concentration | Notes – 3rd quarter results |
| --- | --- | --- | --- | --- |
| Alkalinity | 197 mg/L CaCO3 | 175 mg/L CaCO3 | 91 mg/L CaCO3 | Typical for freshwater; higher during low flow |
| Biological Oxygen Demand | 1.5 mg/L | 1.37 | 2.93 | Slightly above ecoregion mean due to a single elevated sample |
| Cadmium | 0.04 ug/L | 0.04 ug/L | 0.29 ug/L | In compliance with state standard |
| Chloride | 158 mg/L | 126 mg/L | 47 mg/L | In compliance with state standard |
| Chlorophyll-a | 3.7 ug/L | 4.2 ug/L | 9.9 ug/L | Fair level |
| Chromium | 3.3 ug/L | 10.9 ug/L | 4.5 ug/L | In compliance with state standard |
| Conductivity | 1057 mMHOs | 937 mMHOs | 454 mMHOs | Above ecoregion mean, higher during low flow |
| Copper | 2.75 ug/L | 5.4 ug/L | 7.6 ug/L | In compliance with state standard |
| Fecal Coliform Bacteria | 45 CFU/100mL | 240 CFU/100mL | 81 CFU/100mL | In compliance with state standard |
| Hardness | 321 mg/L CaCO3 | 258 mg/L CaCO3 | 129 mg/L CaCO3 | Considered hard water; sometimes very hard during low flow |
| Lead | 0.6 ug/L | 1.8 ug/L | 5.0 ug/L | Exceeds state standard |
| Nickel | 9.6 ug/L | 6.6 ug/L | 7.7 ug/L | In compliance with state standard |
| Nitrogen Ammonia | 107.5 ug/L | 48.0 ug/L | 168.6 ug/L | Exceeds state standard |
| Nitrate + Nitrite | 0.30 mg/L | 2.21 mg/L | 0.30 mg/L | Above ecoregion mean |
| Phosphorus, Total | 0.0938 mg/L | 0.1136 mg/L | 0.1718 mg/L | Slightly above ecoregion mean |
| Suspended Solids | 11.75 mg/L | 50.2 mg/L | 104.1 mg/L | Above ecoregion mean |
| Turbidity | 6.75 NTU | 22.6 NTU | 20.8 NTU | In compliance with state standard |
| Zinc | 7.7 ug/L | 17.2 ug/L | 56.0 ug/L | In compliance with state standard |

mg/L = milligrams per liter or parts per million (ppm)

ug/L = micrograms per liter or parts per billion (ppb)

mMHO = micromhos or microseimens

CFU = colony forming units

NTU = nephelometric turbidity units

Appendix A

Watershed and land use information provided by Metropolitan Council Environmental Services.