Watershed Outlet Monitoring Program

Willow Creek Station

# Burnsville, MN

Quarterly Report

## Preliminary Data

## January – March 2007

Prepared By: Dakota County Soil and Water Conservation District

### Prepared For: Lower Minnesota River Watershed District

##### April 2007

#### Introduction

The Willow Creek WOMP site, located in Burnsville behind the Menards on Hwy. 13, has been in operation since 1999.  The Willow Creek watershed drains more than 5,000 acres of various types of land uses including residential, vacant/agricultural, and commercial properties (Appendix A).  This report summarizes the results of flow, precipitation, and water quality for the 1st quarter of 2007.  This data is preliminary and is subject to change until the Metropolitan Council submits the final report for this period.

#### Flow and Precipitation

Average flow in Willow Creek was 2.99 cubic feet per second (cfs) or 1.93 million gallons per day (mgd) (Table 1).  The rain gauge was not activated until 3/13/07.  A graph describing quarterly flow and precipitation results is also provided (Figure 1).

Table 1. Average flow and total precipitation at Willow Creek WOMP Station January – March 2007

| Period | Average Flow (cfs/mgd) | Precipitation (inches) | *Average Monthly Precipitation, 1997-2006 (inches) |
| --- | --- | --- | --- |
| JANUARY | 1.54/1.00 | NA | 1.02 |
| FEBRUARY | 0.40/0.26 | NA | 0.78 |
| MARCH | 7.27/4.70 | 3.96 | 1.81 |
| TOTAL QUARTER | 2.99/1.93 | 3.96 | 1.19 |

*Average monthly precipitation data obtained from the National Weather Service station located near the Willow WOMP site.

#### Figure 1. Flow and precipitation at Willow WOMP Station January – March 2007

#### Water Quality

Two event composite samples (3/11/07, 3/30/07) and three low flow grab samples were collected at the Willow WOMP Station during the 1st quarter 2007.  Overall, water quality was good with nearly all parameters below the state standard (in compliance with standards) or near the ecoregion mean (Table 2).

Table 2. Average concentrations at Willow Creek WOMP Station October – December 2006 (for comparison purposes) and January – March 2007.

| Parameter | 4th quarter 2006 Ave. Concentration | 1st quarter 2007 Ave. Concentration | Notes – 1st quarter results |
| --- | --- | --- | --- |
| Alkalinity | 273 mg/L CaCO3 | 197 mg/L CaCO3 | Typical for freshwater; higher during low flow |
| Biological Oxygen Demand (BOD5) | 7.7 mg/L | 1.5 mg/L | Below eco-region mean |
| Cadmium | 0.04 ug/L | 0.04 ug/L | In compliance with state standard |
| Chloride | 123 mg/L | 158 mg/L | In compliance with state standard |
| Chlorophyll-a | 2.2 ug/L | 3.7 ug/L | Fair level |
| Chromium | 1.6 ug/L | 3.3 ug/L | In compliance with state standard |
| Conductivity | 1251 mMHOs | 1057 mMHOs | Above ecoregion mean, higher during low flow |
| Copper | 8.7 ug/L | 2.75 ug/L | In compliance with state standard |
| Fecal Coliform Bacteria | 498 CFU/100mL | 45 CFU/100mL | In compliance with state standard |
| Hardness | 483 mg/L CaCO3 | 321 mg/L CaCO3 | Considered hard water; sometimes very hard during low flow |
| Lead | 0.6 ug/L | 0.6 ug/L | In compliance with state standard |
| Nickel | 8.2 ug/L | 9.6 ug/L | In compliance with state standard |
| Nitrogen Ammonia | 123.3 ug/L | 107.5 ug/L | In compliance with state standard |
| Nitrate + Nitrite | 0.76 mg/L | 0.30 mg/L | Above ecoregion mean |
| Phosphorus, Total | 0.2550 mg/L | 0.0938 mg/L | Below ecoregion mean |
| Suspended Solids | 9.3 mg/L | 11.75 mg/L | Below ecoregion mean; higher during some runoff events |
| Turbidity | 4.33 NTU | 6.75 NTU | In compliance with state standard |
| Zinc | 26.0 ug/L | 7.7 ug/L | In compliance with state standard |

mg/L = milligrams per liter or parts per million (ppm)

ug/L = micrograms per liter or parts per billion (ppb)

mMHO = micromhos or micorseimens

CFU = colony forming units

NTU = nephelometric turbidity units

Appendix A

Watershed and land use information provided by Metropolitan Council Environmental Services.