Watershed Outlet Monitoring Program

Willow Creek Station

# Burnsville, MN

Quarterly Report

## Preliminary Data

## January – March 2006

Prepared By: Dakota County Soil and Water Conservation District

### Prepared For: Lower Minnesota River Watershed District

April 2006

The Willow Creek WOMP site, located in Burnsville behind the Cub Foods Store on Hwy. 13, has been in operation since 1999.  This report summarizes the results of flow, precipitation, and water quality for the 1st quarter of 2006.  This data is preliminary and is subject to change until the Metropolitan Council submits the final report for this period.

#### Flow and Precipitation

Average flow in Willow Creek was 2.54 cubic feet per second (cfs) or 1.64 million gallons per day (mgd).  The rain gauge was not activated until 3/31/06.

Table 1. Average flow and total precipitation at Willow Creek WOMP Station January – March 2006

| Period | Average Flow (cfs/mgd) | Precipitation (inches) |
| --- | --- | --- |
| JANUARY | 2.61 / 1.69 | NA |
| FEBRUARY | 1.94 / 1.25 | NA |
| MARCH | 3.02/ 1.95 | NA |
| TOTAL QUARTER | 2.54 / 1.64 | NA |

Figure 1. Flow and precipitation at Willow WOMP Station January – March 2006

#### Water Quality

Two event grab samples (3/24/06, 3/31/06) and two low flow grab samples were taken at the Willow WOMP Station during the 1st  quarter 2006.  Overall, the water quality was fair to good with most parameters below the state standard (in compliance with standards) or near the ecoregion mean (Table 2).

Table 2. Average concentrations at Willow Creek WOMP Station October – December 2005 (for comparison purposes) and January – March 2006.

| Parameter | 4th quarter 2005 Ave. Concentration | 1st quarter 2006 Ave. Concentration | Notes – 1st quarter results |
| --- | --- | --- | --- |
| Alkalinity | 103 mg/L CaCO3 | 148 mg/L CaCO3 | Typical for freshwater; higher during low flow |
| Biological Oxygen Demand (BOD5) | 1.6 mg/L | 1.7 mg/L | Fair level; higher during runoff events |
| Cadmium | NA | 0.04 ug/L | In compliance with state standard |
| Chloride | 57 mg/L | 237 mg/L | Average exceeding state standard; all samples elevated |
| Chlorophyll-a | 20 ug/L | 12 ug/L | Fair level |
| Chromium | NA | 0.6 ug/L | In compliance with state standard |
| Conductivity | 602 mMHOs | 1219 mMHOs | Higher than average for metro streams, and for ecoregion mean |
| Copper | NA | 2.0 ug/L | In compliance with state standard |
| Fecal Coliform Bacteria | 52 CFU | 26 CFU | In compliance with state standard |
| Hardness | 139 mg/L CaCO3 | 198 mg/L CaCO3 | Considered hard water; sometimes very hard during low flow |
| Lead | NA | 0.2 ug/L | In compliance with state standard |
| Nickel | NA | 3.9 ug/L | In compliance with state standard |
| Nitrogen Ammonia | 50 ug/L | 32.5 ug/L | In compliance with state standard |
| Nitrate + Nitrite | 0.32 mg/L | 0.43 mg/L | Above ecoregion mean |
| Phosphorus, Total | 0.18 mg/L | 0.0552 mg/L | Below ecoregion mean |
| Suspended Solids | 56 mg/L | 2.25 mg/L | Below ecoregion mean; higher during some runoff events |
| Turbidity | 12.4 NTU | 3.25 NTU | In compliance with state standard |
| Zinc | NA | 4.3 ug/L | In compliance with state standard |

mg/L = milligrams per liter or parts per million (ppm)

ug/L = micrograms per liter or parts per billion (ppb)

mMHO = micromhos or micorseimens

CFU = colony forming units

NTU = nephelometric turbidity units